## Slide 1: RoadPro
Road builder plugin for AutoCAD
User guide and command shortcuts
Version 3.0 · 07 October 2026
Developed by www.exceltokml.com
Type
RDP
to start
30
!
STOP
CL
Plan view built by one command
Notes: RoadPro builds a complete road drawing in AutoCAD from one centre line: edges, radius, barricades, chainage, signs, sections, cross sections and an Excel report.

## Slide 2: One command builds the complete road
Road and edges
Width both sides of the CL, CL linetype, surface hatch, chainage
Turning radius
Every bend filleted, default 10 m at the centre line
Barricades
Red and white units, black outline, left / right / median
Widening, tapers, junctions
Extra lane (RDW), width change (RDT), junction (RDJ)
Signs and markings
Sign posts and schedule, lane and edge lines, arrows
Radius and sections
C1 curve data and S1 straight data on the plan
Cross sections
Layers, crossfall, barricade and sign heights, dims
Report and Excel
Tables in the drawing plus a CSV file for Excel
Notes: Eight outputs from a single run. Every output sits on its own layer so it can be frozen, plotted or edited separately.

## Slide 3: Install and load in under a minute
1
APPLOAD
Type APPLOAD in the AutoCAD command line
2
Load
Select RoadPro.lsp and click Load
3
Startup
Contents > Add it to the Startup Suite to load in every session
4
RDP
Type RDP to open the RoadPro dialog
Before you start
Full AutoCAD, Civil 3D or Map 3D 2013 or newer (AutoCAD LT is not supported)
Type all sizes in metres. For millimetre drawings choose Millimeters in the dialog
Save the DWG first: the Excel report is saved in the drawing folder
Notes: Adding RoadPro to the Startup Suite means the commands are ready every time AutoCAD opens.

## Slide 4: All commands and shortcuts
FULL COMMAND
SHORTCUT
WHAT IT DOES
ROADPRO
RDP
Build a complete road from a centre line
ROADREPORT
RDR
Report tables and Excel file for any RoadPro road
ROADRADIUS
RDRAD
Add radius, TC / CT and curve data to the plan
ROADSECTIONS
RDSEC
Add straight section labels S1, S2 ... to the plan
ROADXSEC
RDX
Cross sections: typical, one chainage, every interval
ROADWIDEN
RDW
Lane widening with taper, fillet or direct link
ROADTAPER
RDT
Road taper: wider or narrower from any start to end
ROADJUNCTION
RDJ
Join a new road: junction / tie-in with kerb returns
ROADMARK
RDM
Road markings: edge lines, lane line, draw or remove
ROADPRORESET
-
Restore all settings to the factory defaults
Useful AutoCAD keys
U
Undo the whole road in one step
F2
Show the summary and file path
Enter
Finish the centre line or skip a prompt
Esc
Cancel the command
Notes: The short versions in red are the fastest way to work. U undoes the complete road because RoadPro wraps everything in one undo group.

## Slide 5: From centre line to finished drawing in six steps
1. Set options
RDP opens the dialog. Defaults are ready, press OK
2. Centre line
Pick points (Arc allowed, Enter to finish) or select a line
3. Auto build
Radius, edges, CL, surface, barricades, chainage
4. Signs and ends
Signs with IDs, tie-in or road closed, lane arrows
5. Report
Summary on screen, Excel file saved, place tables
6. Cross section
Pick a point to place the typical section
Tip: the whole sequence runs from one command. Steps 5 and 6 ask for a placement point; press Enter to skip the drawing tables or the section. The Excel file is saved either way.

## Slide 6: Dialog settings: road geometry and barricades
Road Geometry
Road name / ID
ROAD-01
Road width
7.30 m
Turning radius
10.0 m
Radius measured at
Centre line (CL)
Drawing units
Meters or Millimeters
Centre line input
Pick points or select
Radius, TC / CT on plan
On
Straight sections on plan
On
Barricades
Sides
Left + Right (Centre optional)
Unit length
2.00 m
Unit width
0.50 m
Gap from road edge
0.50 m
Fill and outline
Red / white, black
Units alternate red and white. The count of each colour is in the report for ordering.
Notes: From v2.5 the turning radius is measured at the centre line by default. Choose Inner edge (kerb line) in the same dropdown if your design gives the kerb radius; the centre line then gets R plus half the width.

## Slide 7: Dialog settings: signs, surface, chainage and outputs
Signs and Markings
Speed limit
30 km/h
Bend ahead
30 m before
Road works ahead
On
Chevron boards
On
Keep right (median)
On
Lane arrows
On
At tie-in
STOP / GIVE WAY
Symbol / spacing
2.0 m / 15 m
Surface and Chainage
Hatch road surface
SOLID, 50%
CL text in line
On
Chainage marks
On
Interval
20 m
Start chainage
0 m
Text height
1.0 m
Road Ends and Outputs
Start end
Tie-in line
Finish end
Tie-in line
Other options
Closed / None
Report + Excel
On
Typical section
On
Two-way traffic
On

## Slide 8: Everything on its own layer
ROAD-CL
Centre line, CL linetype
ROAD-EDGE
Left and right edges
ROAD-SURFACE
Surface hatch
ROAD-BARRIER-RED
Red barricade fill
ROAD-BARRIER-WHITE
White barricade fill
ROAD-BARRIER-OUTLINE
Black outline
ROAD-CHAINAGE
Ticks and labels
ROAD-CURVE
Radius, TC / CT, C1
ROAD-SECTION
Straights S1, S2
ROAD-SIGN*
Posts, plates, symbols
ROAD-MARKING*
Lane arrows
ROAD-TIEIN
Tie-in line and E / N
ROAD-REPORT
Tables and legend
ROAD-XSEC*
Cross section parts
ROAD-WIDENING
Widening / taper labels
ROAD-JUNCTION
Junction labels, corner R
Notes: Freeze, lock or switch off any group to plot only what you need. White fills plot as white with the black outline.

## Slide 9: Signage placed automatically, traffic keeps right
!
Road works ahead
Entry of each direction
30
Speed limit
One spacing after entry
↱
Bend ahead
Before each bend
STOP
STOP
Before each tie-in
Give way
Option at tie-ins
No entry
Far end, one-way road
Keep right
Median nose
How each sign is drawn on the plan
30
SG-01
Post and plate
Black dot outside the barricade, plate faces the traffic
Leader, symbol and ID
IDs SG-01, SG-02 ... follow the chainage order
Also drawn
Chevron boards on the outside of bends
ROAD CLOSED boards at closed ends
White lane arrows on straights
Sign schedule with E / N of every post
Notes: Sign types and distances are a sensible default. Check them against the approved Traffic Management Plan and Qatar work-zone guidelines before issue.

## Slide 10: Radius and road sections on the plan
Every curve
RDRAD
C1
R inner = 10.000 m
R CL = 13.650 m
R outer = 17.300 m
L (CL) = 21.441 m
A = 156.52 m²
Δ = 90°00'00"
Radius line with arrow from the centre point, R value on the line, TC and CT ticks across the road with chainage.
Every straight
RDSEC
S1 STRAIGHT
L = 45.230 m
A = 330.18 m²
CH 0+012.000 - 0+057.230
BRG 45°12'30"
Extent bar with end ticks on the right side, label parallel to the road. Bearing is whole-circle from North.
Notes: Curve numbers C1, C2 and straight numbers S1, S2 match the Curve Data and Road Sections tables in the report.

## Slide 11: Cross sections with widths and heights
CL
30
Carriageway 7.30 m
H 1.00
2.5%
2.5%
Sign 2.10 m clear
Typical section (simplified)
RDX
Three ways to draw
1
Typical
One generic section for the whole road
2
One chainage
Type the chainage, note shows curve or straight
3
Every interval
A sheet of sections, 3 per row, up to 60
Defaults: crossfall 2.5%, layers 50 / 200 / 150 mm, barricade 1.00 m high, sign clearance 2.10 m. Replace with your project values.

## Slide 12: Lane widening with tapers and match points
Plan view (right side widening)
TS
FS
FE
TE
Taper in
Full extra width (start to end chainage)
Taper out
+3.65
Straight + fillet
Arc with radius R at all 4 match points (TS, FS, FE, TE). Too big? RoadPro reduces R to fit.
Straight + direct link
Sharp joints. The straight taper meets the edge directly at the match points.
Curve taper
Two reverse curves per taper, tangent at the match points, so no fillet is needed.
RDW
Select the centre line
Side
Left / Right / Both
Extra width
3.65 m
Start / end chainage
your input
Taper in / out
30 m / 30 m
Taper type
Straight or Curve
Match point
Fillet R or Direct link
Fillet radius
30 m
Barricades
moved to new edge
Both sides
own chainage + R
Also drawn: new edge, lane surface, lane arrow, width dimension, match points and R=.. radius marks. Run RDW again for more sections (W1, W2 ...).
Notes: Start and end chainage are where the full extra width begins and ends. The tapers are added before the start and after the end. The widening follows straights and bends of the road.

## Slide 13: Road taper anywhere: wider or narrower
Plan view (both sides, edge +1.00 m)
TS
TE
7.30 m
9.30 m to the road end >
Start CH
End CH
Any start and end
Put the taper at any chainage: start, middle or end of the road.
Tapers add up
Run RDT again anywhere. 7.30 > 9.30 m, later 9.30 > 7.30 m.
Wider or narrower
+ shift adds hatched surface, - shift wipes the old surface out.
RDT
Select the centre line
Side
Left / Right / Both
Taper start chainage
your input
Taper end chainage
your input
Edge shift per side
+ wider / - narrower
Taper type
Straight or Curve
Match point
Fillet R or Direct link
Fillet radius
30 m
Barricades
follow new edge
Both sides
own chainage + R
RDW = extra lane that comes back. RDT = width change that continues. Keep them on different chainage ranges of the same side.
Notes: If a narrowing would bring the edge too close to the centre line, RoadPro stops and shows the chainage. Each run rebuilds that side's edge, surface, barricades and labels from all its tapers together.

## Slide 14: Chainage input, both sides and radius marks
1. Type chainage your way
100
=
0+100
1250
=
1+250
1250.5
=
1+250.5
The taper is added outside your chainages:
70
100
180
210
Start 100, End 180, tapers 30 m. Keep Start ≥ taper in, and End + taper out ≤ road end.
2. Both sides, own values
Side = Both sides, then tick Different chainage on right side.
LEFT
RIGHT
Start / End
100 / 180
150 / 260
Taper in / out
30 / 30
20 / 40
Fillet radius
30 m
15 m
Extra width
3.65 m
3.65 m
Works in RDW and RDT. Each side gets its own match points, labels and report rows (W1-L, W1-R).
3. Every radius marked
R=30.00
Straight + fillet: R at every fillet
Curve taper: R on each reverse-curve arc
Direct link: no radius, no mark
Arrow points to the new edge, text on the pavement side. If RoadPro had to reduce R, the mark shows the real R drawn.
Notes: Chainage boxes accept plain metres or chainage format. The right-side panel is only active with Side = Both sides and the tick on. Radius marks are on layer ROAD-WIDENING.

## Slide 15: Road junction / tie-in with kerb returns
Plan view (branch on the left side)
R=10
R=10
ROAD-01 (main)
ROAD-02
J1
STOP
Start on the main CL
Draw the branch from the main road centre line outward, or select a line.
Everything automatic
Edge opened, kerb returns, corner surface, barricades and STOP / GIVE WAY.
Report and setting-out
TC, IP and CT of each corner with E / N, in Excel and in the drawing.
RDJ
Select the MAIN road
Branch name
ROAD-02
Branch width
7.30 m
Branch centre line
Draw or select
Corner (kerb) radius
10 m
Control on branch
STOP / GIVE WAY
Corner barricades
On
Branch chainage
0+000 at junction
Angle
any (skew OK)
Turning-area markings
On
Run RDJ again for more branches (J1, J2 ...), on either side. For a crossroads add one branch on each side at the same chainage.
Notes: The branch is a full RoadPro road built with the RDP settings. Build the junction where the main road has its normal edge, not inside a widening or taper range on that side.

## Slide 16: Road markings: lines, arrows and paint quantities
Along the road
Broken lane line 3 m / 6 m
Solid on bends and junction approaches
Turning area of a junction (RDJ)
STOP
Stop line + STOP (or give-way line + triangle), left / right turn arrow, broken edge line across the mouth.
RDM
Draw or Remove
Line colour / width
White, 150 mm
Edge lines
0.30 m inside edge
Lane line
Broken 3 m / 6 m
Solid lane line
Bends +/- 10 m
Junction approach
Solid 16 m
With median
No lane line
Junctions
Edge line gap
Report
Length + m2 paint
New roads: tick Road markings in the RDP dialog. Existing roads: run RDM. RDJ redraws the markings of both roads with the junction gaps.
Notes: Run RDM again after tapers or junctions and it replaces the old markings cleanly. Edge lines follow road tapers.

## Slide 17: Report and Excel file
Summary
General, geometry, barricades, signs, road ends, chainage
Curve data
TC / CT chainage, radius, arc, deflection, E / N
Road sections
Every straight and curve: length, edges, area
Setting-out
E / N of CL, left and right edge at every chainage
Sign schedule
ID, sign, chainage, side, facing, post E / N
Widening, taper and junction setting-out
New edge offset, kerb returns TC / IP / CT with E / N
Road markings
Edge and lane line lengths, paint area in m2
Where is the Excel file?
ROAD-01_RoadPro_Report.csv
Saved in the same folder as the DWG
Enter only skips the drawing tables, never the Excel file
Close the old CSV in Excel before running again
Press F2 to see the full path
Run again any time:
RDR

## Slide 18: Quick fixes for common questions
Unknown command RDP
Load RoadPro.lsp with APPLOAD. Full AutoCAD only, not LT
Road is 1000 times too small or big
Choose Millimeters in Drawing units for mm drawings
Turning radius is too small
At the centre line, R must be more than half the road width
Black outline not visible
Dark background on screen. It still plots black
Excel file could not be saved
Close the old CSV in Excel, then run RDR again
Junction not formed
Start the branch ON the main road CL, away from widened or tapered edges
Widening runs outside the road
Start must be at least the taper in; End + taper out within the road
Chainage not accepted
Type 100 or 0+100. Older versions take plain metres only

## Slide 19: Quick reference card
RDP
Build road
RDR
Report + Excel
RDRAD
Radius labels
RDSEC
Straight labels
RDX
Cross sections
RDW
Lane widening
RDT
Road taper
RDJ
Junction / tie-in
RDM
Road markings
U
Undo whole road
F2
Summary + path
Default values
Road width
7.30 m
Turning radius
10 m at CL
Barricade unit
2.0 x 0.5 m
Chainage
every 20 m
Speed limit
30 km/h
Crossfall
2.5%
Widening / taper
3.65 m / 30 m
Reset all
ROADPRORESET
Type RDP, accept the defaults, draw the centre line. RoadPro does the rest.
Developed by https://www.exceltokml.com/